ATTACHMENT I

Emergency Procedures

Minor Spills (<200 ml and < 100 mCi/ml)

1.  	NOTIFY - Notify persons in the area that a spill has occurred.

2.	PREVENT THE SPREAD - Cover the spill with absorbent.

3.	CLEAN UP – Wear appropriate PPE including disposable gloves.  Carefully fold the absorbent paper

and pad.  Insert into a plastic bag or other suitable container and dispose in the radioactive waste container.  	Also insert into the plastic bag/container all other contaminated materials such as disposable gloves.

4.	SURVEY - with an appropriate contamination survey instrument for the nuclide(s) involved in the spill, 	checking the area around the spill area, hands, and clothing for contamination.

5.	REPORT - Report incident to the Radiation Safety Officer.

Major Spills (>/= 200 ml or >100 mCi/ml)

1.	CLEAR THE AREA - Notify all persons not involved in the spill to vacate the area.

2.	PREVENT THE SPREAD - Dam the spill with absorbent, but do not attempt to clean it up.

Confine the movement of all potentially contaminated personnel to prevent any spreading.

3.	SHIELD THE SOURCE - If possible, the spill should be shielded, but only if it can be done without 	further contamination or without significantly increasing your radiation exposure.

4.	SECURE THE AREA - Leave the area and lock the door(s) to prevent entry.

5.	CALL FOR HELP - Notify the Radiation Safety Officer immediately.

6.	PERSONNEL DECONTAMINATION - Contaminated clothing should be removed and stored for further 	evaluation by the Radiation Safety Officer.  If the spill is on the skin, flush thoroughly with lukewarm water 	and then wash with mild soap and lukewarm water.

| Radiation Safety Officer |  |
| --- | --- |
| Office Phone |  |
| Home Phone |  |

Attachment I – continued

Loss, Theft, Fire, Explosion, or Vehicle Accident

Follow the procedures outlined in the Washington State Department of Health - Radiation Emergency Handbook.   Principally this shall include:

1.  	Secure the area around the accident.   Keep unauthorized persons away.   Alert people in the vicinity 	as to the presence of radioactivity and a possible hazard.

2. 	DO NOT leave the site.  Send a helper or onlooker to notify the following:

a.    Radiation Safety Officer

Work Phone        Home Phone

b.    Local Police

c.    Local Fire Department, where applicable

3.	The Radiation Safety Officer, in turn, must immediately notify the State of Washington Radiation 	Emergency Response at (206) 682 - 5327, which is

206  N-U-C-L-E-A-R

and other local authorities, as indicated.

4.	The radiation worker should inform emergency workers of the radiation hazard possibly existing, should 	help them keep the area secure, and should explain to the emergency personnel the location of the 	radioactive device or chemical and the extent of the possible hazard.  In no case should the radiation 	worker leave the site until qualified experts arrive, unless, of course,  said worker is seriously injured or 	incapacitated, and must be removed from the site by emergency personnel.

Alternate Names and Telephone Numbers Designated by Radiation Safety Officer

| APPROVED BY |  | DATE |
| --- | --- | --- |